Names: Robin Singh, Jose Alex Colon
Date: 12/15/2023
CPE 301
Final Project Overview

Experimental Design:

This project entailed the conceptual construction of a swamp cooler. A circuit was built that was comprised of a temperature and humidity sensor, a water level sensor, a real time clock and LCD (used for reporting a change of states), stepper motor and DC motor for operating vent position and a fan for cooling, four LEDs are used for signaling the current state as well as several buttons for “start”, “stop” and “reset”.

In the Disabled state a yellow LED is on until the “start” button is pressed. When the “start” button is pressed the system goes into the Idle state where the green LED goes on.

In the Idle state the temperature and water level are frequently checked. If the water level is too low an error message is displayed on the LCD. If the temperature is below 15 C, the system remains in the Idle state . If the temperature is above 16 C, the system goes into the Running state.

In the Running state a blue LED is displayed. In the Running state the temperature and water level are frequently checked. If the water level is too low an error message is displayed on the LCD. If the temperature falls below 15 C, the system goes back tho the Idle state. Pushing the “stop” button puts the system back into the Disabled state.

In the Error state(Red Led), pushing the “stop” button put the system back into the Disabled state. Pushing the “reset” button puts the system into the Idle state.

Operating Temperatures: System is on >= 16 Celcius, below 15 Celsius, system is off.
Water level low (Error message): System is off
Power Requirements: 5 V

References:

LCD https://datasheetspdf.com/datasheet/LCM1602A.html
DHT11 https://components101.com/sensors/dht11-temperature-sensor
Real Time Clock https://www.analog.com/media/en/technical-documentation/data-sheets/ds3231.pdf
Water Level Sensor http://shop.alsrobot.com/wiki/index.php/(SKU:RB-02S048)Water_Sensor
Stepper Motor Driver https://www.electronicoscaldas.com/datasheet/ULN2003A-PCB.pdf
DC Motor Driver https://www.ti.com/document-viewer/l293d/datasheet
Stepper Motor https://www.mouser.com/datasheet/2/758/stepd-01-data-sheet-1143075.pdf
DC Motor https://www.adafruit.com/product/711
Button https://einstronic.com/product/tactile-push-button-6x6xh5-red/
RGB LED https://www.kingbright.com/attachments/file/psearch/000/00/20160808bak/L-154A4SURKQBDZGC(Ver.12A).pdf